## Slide 1: GESTURE RECOGNIZATION VIA TINYML
Submitted by: Amulya Yadagani
Mentored by: Dr.Somya Mohanty
30/11/2020

## Slide 2: OUTLINE
Introduction
Goals
Challenges
Methodology Workflow
  Data Collection
Deep Learning Workflow
  Data Preprocessing
  Train, Test, Validation Sets
  Building Deep Learning Model
  Compiling & Fitting the model
  Model Pruning & Quantization
  Model Inference
Results
Conclusion
Reference

## Slide 3: Introduction
Machine Learning on Microcontrollers is the most efficient, cheap, and reliable way of developing Edge Computing applications with low energy consumption.
‘Arduino Nano 33 BLE Sense board’ is used as a microcontroller to capture and classify 5 human gestures - “Squat”, “Jump”, “Walk”, “Run”, “Other”.
The board has capabilities such as embedded sensors and BLE enabled.
Built Deep Learning model using captured gestures data to classify human gestures

## Slide 4: Microcontroller - Arduino Nano 33 BLE Sense

## Slide 5
Tiny form factor having 45x18mm dimensions
9 on-board sensors, in this research accelerometer and gyroscope inertial sensors are used.
Nordic nRF52840 processor
  32-bit ARM Cortex M4 CPU
  NINA B306 module for BLE
  SRAM : 256KB
  Flash Memory : 1MB
  Operating Voltage : 3.3V

## Slide 6: Goals
To showcase the following benefits in developing Edge Computing applications without sacrificing accuracy on Microcontrollers such as Arduino Nano 33 BLE Sense board:
  Cost Effective
  Low Energy Consumption
  Data Privacy
  Tiny form factor
  Flexibility

## Slide 7: Challenges & Workaround
Challenge 1: Capturing Training Data from the Arduino Board
Workaround: Python script to capture data via BLE
Challenge 2: The size of the traditional Machine Learning model is huge, loading the model onto the microcontroller
Workaround: Pruning and Quantization techniques to reduce model size
Notes: Publically available dataset deidentify

## Slide 8: Methodology Workflow

## Slide 9: Data Collection
The board is programmed to capture the 3-axis accelerometer and a 3-axis gyroscope data using the inertial sensors (IMU)
  Accelerometer range is set at [-4,+4]g -/+0.122 mg
  Gyroscope range is set at [-2000, +2000] dps +/-70 mdps
  Magnetometer range is set at [-400, +400] uT +/-0.014 uT
IMU Sampling Rates : [10Hz, 50 hz, 119 hz, 238 hz, 476 hz, 952 hz]
Each gesture is performed 100 times with a sampling rate of 119 Hz and a minimum Threshold of 1.5

## Slide 10
Data transferred via BLE from board (central) to the system (peripheral)
Python script to discover BLE device and establish connection using devices GATT services and its characteristics
For a gesture, data is sent continuously until all samples (119) are read.
The data is sent in the form of a string

## Slide 11
BLE connected

## Slide 12: Deep Learning WorkFlow

## Slide 13: Data Preprocessing
Deep learning models accept input and generate output in the form of tensors
Transformed the input into tensor with shape (500, 716)
  500 : 100 samples for each of 5 gestures
  716 : each sample rate X (accelerometer,gyroscope) = 119 x 6 = 716
Transformed the output into tensor with shape (500, 5)
  500 : 100 samples for each of 5 gestures
  5 : one-hot encoded matrix for each of 5 gestures

## Slide 14: Train, Test and Validation Sets
Shuffle input and output data
Shuffled data is split into
  60% training
  20% test
  20% validation

## Slide 15: Building Deep Learning Model
Consists of total 7 layers
  4 are "Dense" layers (nodes per layer: 100, 75, 75, 5)
  3 are "Dropout" (0.15)
Rectified linear activation function (ReLU) outputs the input directly if it is positive or it will output zero

## Slide 16: Compiling and Fitting the model
Compiling the model takes 3 parameters - optimizer, loss, metrics
  “Adam” optimizer with learning rate=0.0001
  “mean_squared_error” as a loss function
  “accuracy” of model as metrics
“ ReduceLROnPlateau” is used as a callback to reduce the learning rate when a metric has stopped improving

## Slide 17: Model Pruning and Quantization
why?
  Reduces model size
  Faster Execution
  Reduces Power consumption
Pruning is an iterative process on a trained model that trims insignificant weights by setting those weights to zero until specified target sparsity
Removes unnecessary connections between the layers

## Slide 18
Quantization is a process where the weights are converted to lower-precision types, such as from float32 to int8.
How it works?
  Take only the required range used by Float32 to represent in smaller no of bits
  Required Range : Histogram distribution of values in a particular tensor by grouping data into 255 bins which is integer equivalent.
  quantized_value = float_value / scale + zero_point
    scale = (max - min)/ 2^bits (Floating point size of each bin)
    zero_point = integer zero that corresponds floating point zero

## Slide 19: Model Inference
Board is programmed to use the trained TensorFlow Lite model for the classification of gestures
Board is programmed with
  static tensor size (40x1024),
  string characteristic UUID to transfer the output
  an interpreter to run the deep learning model
Highest probability gesture indicated by LED light and transmitted via Bluetooth.

## Slide 20: Gestures LED color
Gesture | LED Color
Squat | Red
Jump | Magenta
Walk | Blue
Run | Green
Other | White

## Slide 21: Gestures Output

## Slide 22: RESULTS

## Slide 23: Data Collection Results
Visualization of Squat Data - One Sample

## Slide 24: Visualization of Squat Data - 100 Samples

## Slide 25: Visualization of Jump Data - One Sample

## Slide 26: Visualization of Jump Data - 100 Samples

## Slide 27: Visualization of Walk Data - One Sample

## Slide 28: Visualization of Walk Data - 100 Samples

## Slide 29: Visualization of Run Data - One Sample

## Slide 30: Visualization of Run Data - 100 Samples

## Slide 31: Visualization of Other Data - 100 Samples

## Slide 32: Training and validation loss of the trained model
Deep Learning Results

## Slide 33: Training and validation Accuracy of the trained model

## Slide 34: Confusion Matrix of the trained model

## Slide 35: Size, Accuracy and Confusion Matrix of the compression model
Size of the model is reduced 4 times from 2.1Mb to 0.5Mb
96% accuracy

## Slide 36: Predicting Squat gesture
Demo

## Slide 37: Predicting Jump gesture

## Slide 38: Predicting Walk gesture

## Slide 39: Predicting Run gesture

## Slide 40: Conclusion
This research work shows us how simple and efficient it is to achieve an end to end application involving deep learning to predict human gesture with real data.
Gestures application showcases all the benefits the microcontroller offers as mentioned in goals
Along with the benefits, the tiny form factor and embedded sensors can be used as a wearable device and therefore used in building multiple real-world applications

## Slide 41: References
1. https://www.arduino.cc/en/Guide/NANO33BLESense
2. https://blog.arduino.cc/2019/10/15/get-started-with-machine-learning-on-arduino
3. https://bleak.readthedocs.io/en/latest/
4. https://github.com/hbldh/bleak
5. https://keras.io/api/
6. https://www.tensorflow.org/model_optimization/guide/pruning/pruning_with_keras
7. https://www.tensorflow.org/model_optimization/guide/quantization/post_training

## Slide 42: Git URL
https://github.com/UNCG-DAISY/Tiny_Gesture

## Slide 43: QUESTIONS ?

## Slide 44: THANK YOU